## Slide 1: Contaminants of emerging concern
Air and waste management association
November 22, 2019
Ed Putnam, Assistant Director
Ed.Putnam@dep.nj.gov

## Slide 2: What are contaminants of emerging concern? (a.k.a. Emerging contaminants) As science improves it allows regulators and health specialist to better evaluate the health risks presented by existing and new chemicals. Technology improvements allow us to detect these chemicals at lower and lower detection limits.

## Slide 3
There will always be contaminants of emerging concern.
This presentation is limited to these compounds in Groundwater and drinking water;
  1,4 dioxane
  PFAS
  123 TCP
  perchlorate

## Slide 4: 1, 4 dioxane
Primarily a stabilizer added to chlorinated solvents, particularly 1,1,1- trichloroethane
Can be a byproduct in Consumer products.
Completely immiscible in water

## Slide 5: 1,4 dioxane
Previously the interim GWQS was 10 ppb
UCMR 3 175 systems sampled; zero over 10 ppb
Groundwater quality standard- 0.04 ppb
UCMR 3; 31 of 175 tested over 0.04 ppb

## Slide 6: 1, 4 dioxane
Has been referred to the DWQI- no schedule for MCL.
GWQS is effective and enforceable since 2015
EPA method 522

## Slide 7: 1,4 dioxane where would you find it?
1,1,1 TCA is the most likely culprit.
Other chlorinated solvents
Landfills (consumer products)
wastewater

## Slide 8: 1,4 dioxane treatment
Advanced Oxidation
Resins
Bacteria

## Slide 9: PFAS (per and polyfluoroalkyl substances)
“forever chemical”
“ found everywhere”
Anything slippery, waterproof, stain resistant.
AFFF , electroplating.

## Slide 10: PFAS regulations
Currently only PFNA is regulated in drinking water, gwqs. PFOA/PFOS interim gwqs
PFOA and PFOS will go final in the spring.
Drinking water, NJDPES, gwqs, PWTA

## Slide 11: PFAS
EPA method 537
Treatment - activated carbon, resin
More to come

## Slide 12: 1,2,3 TrichloroPropane
Limited industrial use
Manufacturing by product of di-chloropropane or di-chloropropene
Di-chloropropene compounds used as fumigants

## Slide 13: 1,2,3 TrichloroPropane
Drinking water method 504. also shows EDB and DBCP
MCL is a PQL and subject to change
PWTA
So far not significant

## Slide 14: perchlroate
Fertilizer
“energetic compounds”
GWQS
EPA considering MCL, method 314
treatment

## Slide 15: Additional resources
https://clu-in.org/
https://www.itrcweb.org/
https://www.nj.gov/dep/srp/emerging-contaminants/
https://www.epa.gov/wqc/contaminants-emerging-concern-including-pharmaceuticals-and-personal-care-products

## Slide 16
Questions?